Stepper Based Multifunction Plotter

# Introduction
### Getting started
The idea of building a SMPB, arises due to the need for a means which allows easy production of PCBs for future prototypes. (Although not rule use in other applications beyond fiberglass and copper.)

The most important objective will be the accuracy gained, hoping to plot tracks of a minimum size of 0.2 to 0.4 mm. Enabling simple PCB trace for multiple applications.
### How it works

The SMPT is composed by 5 main function stages, starting from the surce software and finishng at the final product or phisical element. Althougth must build a propper power supply device.

Computer
managed
control
Serial
interface
RS-232
Microcontroler
buffer & order
decoder
Power stage
Stepper and
drilling device

CMC
SI
BOD
PS
SBDD

- Computer Managed Control [CMC]
  The proccess starts here. A PC software interprets the plotting program witch contains the design of the proyect-to-plot.
- Serial Interface [SI]
  Stage who transforms TIA/EIA-232-F inputs to 5-V TTL/CMOS levels & viceversa.
- Buffer & Order Decoder [BOD]
  This stage will be responsible of decoding the orders set the program to run, Furthermore, this step function as buffer storing sets of commands in your ram. The device will be composed of one or more microcontrollers.
- Power Stage [PS]
  It will manage power switches, controlled by microcontroler decoded instructions, in order to supply the motor coils when needed.
- Stepper Block and Drilling Device [SBDD]
  All drills and Stepper motors are in that block, in with will be hardest mechanical work.
# Function blocks
## Computer Managed Control [CMC]

## Serial Interface [SI]

## Buffer & Order Decoder Block [BODB]

### BOD interpreter and ORDER statement

In this block will stablish the sequences that take place on SBDD , also will function as buffer storing in RAM, the sets of instructions sent by the CMC block.

Speed of the transmision will be 9600 baud. 1200 bytes per second. [ real data transmit rate will be less due to system delays and waitings].

The serial data transmission is composed by a "string" of 8 bytes which establishes a set of parameters, these are shown in the table and lines below.

### Byte 1
Fixed value for order start.
### Byte 2
Select the edge will receive that sending order.
### Byte 3
Select the action will realize the selected edge.
### Bytes 4:7
- They will set pulse quantity will send to the stepper motors with a resolution of xx mm an a range from 1 to 261.120 pulse, with a step of 1 but there are a lot of imposible values so user should play with them and if its neccesary use two ORDERS to accurate the desired value.

First, the user must know and take care some rules.
- Take care about the data types and their data ranges
  OQUANT must be 0<>1023
  OMULT must be 0<>255
  OADD must be 0<>255
- The algoritm of the pulse quantization is below.

Pq=(Q*M)+A
Where Pq is final pulse quanity, Q is quantity, M is multyplier, and A is the amount to add

Calculate examples below
Q=1 / M=1 / A=0	(Q*M)+A=Pq / (1*1)+0=1

Q=1023 / M=255 / A=255	(Q*M)+A=Pq / (1023*255)+255=261.120

### BOD Decoding process

Keep in mind that unipolar stepper motors using sequences have a certain number of pulses that vary depending on the tool axis and used.

Commonly used sequences of 8 pulses.
We will have to know by software position in which the stepper stay after the last order received. That will have to be between 1 and 8.

And the next order witch affect the same Stepper must start from the next of the last position.
### Communication between Computer Managed Control , Buffer & Order Decoder and Stepper Block and Drilling Device [CMC], [BOD] and [SBDD]

Once the order decoded had get the selected steppers last position must do the select the correct step of the sequence in order to start from the last known position of the motor.

Pq is pulse quantity [between 1-261.120]
P is position [between 1-8]